## Slide 1
For counter-current liquid-liquid extraction, the flow rate difference of passing streams (such as E1 and R2) remains constant throughout the entire cascade.
true
false
depends on the maximum solubility of the contaminant
1
2
extract
raffinate
E1
E2
R2
R1
Notes: 1

## Slide 2
Using a graphical method for counter-current cascades in a partially miscible system, streams exiting the same stage (such as E1 and R1) are connected by __________.
the difference point
equilibrium curve
neither of these
1
2
extract
raffinate
E1
E2
R2
R1
Notes: 2

## Slide 3
Given a constant liquid-liquid extraction partition coefficient, the flow rates of solute (B) and liquid carrier (A), how can one decrease the concentration of B in the raffinate stream?
Assume equilibrium is reached at each stage.
increase the tank size
decrease the amount of solvent
increase the amount of solvent
recycle ½ of the raffinate to the feed
Notes: 3

## Slide 4
A liquid-liquid extraction of a solute (B) in a feed carrier (A) is performed using a solvent (S). Which of the following, when doubled, will have the greatest impact on increasing the fraction of B extracted?
flow rate of A
flow rate of S
reciprocal of the partition coefficient
mass ratio of B to the feed (A)
Notes: 4

## Slide 5
Which of the following material balances is true for a co-current liquid-liquid extraction with stage equilibrium?
R1 = R2
R1 + R2 = E0 + E1
E0 + R1 = E1 + R2
E0 + R2 = E1 + R1
Stage 1
Stage 2
R1
RN
R2
Stage N
RN+1
E0
E1
EN
EN-1
Notes: 5

## Slide 6
Vitamin E is isolated from a vegetable oil using hexane in liquid-liquid extraction. How may degrees of freedom does this system have? The mixed feed contains oil, hexane and vitamin E.
0
1
2
3
4
Mixed feed
Extract
Raffinate
X wt.% oil
Y wt.% C6
Z wt.% Vit.E
Settling Tank
Temp = 25°C
Notes: ANSWER: C. There are 3 components all in liquid phase, however 2 liquid phases are created. Thus there are 3 degrees of freedom for the mixture. However, temperature is specified, so there are 2 more DOF.
𝐷𝑂𝐹=𝐶−𝑃+2
𝐷𝑂𝐹=3−2+2=3
6

## Slide 7
Which of the following will reduce the fraction of solute in the extract stream for a multiple-stage, liquid-liquid extraction? Assume the partition coefficient is > 1, all else is held constant, and two phases are created.
increase the fraction of solute in the feed
decrease the amount of solute in the raffinate
decrease the solvent to feed ratio
decrease the purity of the solvent (with more solute)
none of the above
Notes: 7

## Slide 8
What species is the solute?
ethylene glycol
water
furfural
cannot tell
ethylene glycol
water
furfural
Notes: 8

## Slide 9
Which system will have a mixture separate into an extract and raffinate phase with equal compositions?
(T – solute, H – carrier, S – solvent)
T
T
S
H
H
A
B
Both A & B
S
C
Notes: 9

## Slide 10
T
H
S
Which system has a greater partition coefficient for the solute (T) in the solvent (S)? Note: H is the carrier fluid.
S
S
H
H
T
T
A
B
C
D
Cannot tell from plots
Notes: 10

## Slide 11
What is the maximum amount of the solute T in the feed that can enter an extraction unit if using pure solvent? H is the carrier and S is the extracting solvent.
100%
85%
65%
40%
0
0
0
20
20
20
40
40
40
60
60
60
80
80
80
100
100
100
T
S
H
Notes: 11

## Slide 12
Which axis represents the solute (S)?
High S
Low S
High S
Low S
A
B
C
Notes: 12

## Slide 13
Which stream has the highest flow rate?
solvent
feed
extract
raffinate
more than one are highest
Chart: Wt.% of Isopropyl Alcohol
| 0 | 10 | 20 | 30 | 40 | 45.5 | 40 | 30 | 20 | 10 | 0
 | 1 | 2 | 3 | 5.4 | 12 | 30 | 46 | 62 | 76 | 88 | 100
 | 100 | 0
 | 100 | 0
 | 76 | 1.9
extract
Notes: 13

## Slide 14
For a dilute system, for which separation processes can we not assume constant flow rates?
immiscible liquid-liquid extraction
stripping
partially miscible liquid-liquid extraction
absorption
washing
Notes: 14