## Slide 1
Which two streams relate to equilibrium conditions for equilibrium staged operations?
2 & 5
1 & 2
2 & 6
2 & 4
Stage A
Stage B
1
2
3
4
5
6

## Slide 2
Which two streams relate to operating conditions for equilibrium staged operations?
2 & 5
1 & 2
2 & 6
2 & 4
Stage A
Stage B
1
2
3
4
5
6

## Slide 3
Which of the following relationships is true using the distillation setup shown?
K = thermodynamic K-value
N
N-1
2
1
Total reboiler
Total condenser
Notes: ANSWER: B. The K-value is a ratio between the vapor mole fraction (y) and the liquid mole fraction (x) on a given equilibrium stage. 𝑦_1=𝐾_1 𝑥_1 . Knowing at the operating stage (between equilibrium stages) that the vapor and liquid mole fractions are the same (y1 = x2) we can show:
𝑦_1=𝑥_2; 𝑦_1=𝑥_2=𝐾_1 𝑥_1

## Slide 4
Consider the mass/energy balance envelope constructed around the feed stage of a distillation column. As the feed quality increases, the molar flow rate of the liquid stream _________.
increases
decreases
remains the same
V
L
F, q

## Slide 5
Chart: xMethanol
| 0 | 1.2E-2 | 0.02 | 2.5999999999999999E-2 | 3.3000000000000002E-2 | 3.5999999999999997E-2 | 5.2999999999999999E-2 | 7.3999999999999996E-2 | 8.6999999999999994E-2 | 0.108 | 0.129 | 0.16400000000000001 | 0.191 | 0.26800000000000002 | 0.29399999999999998 | 0.35199999999999998 | 0.40200000000000002 | 0.45400000000000001 | 0.502 | 0.56299999999999994 | 0.624 | 0.71699999999999997 | 0.79 | 0.84299999999999997 | 0.85699999999999998 | 0.93799999999999994 | 1
 | 0 | 0.068 | 0.121 | 0.159 | 0.188 | 0.215 | 0.275 | 0.356 | 0.395 | 0.44 | 0.488 | 0.537 | 0.572 | 0.648 | 0.666 | 0.704 | 0.734 | 0.76 | 0.785 | 0.812 | 0.835 | 0.877 | 0.91 | 0.93 | 0.939 | 0.971 | 1
A McCabe-Thiele solution to a distillation column separating methanol and water is shown. The blue line is the top operating line and the green line is the bottom operating line. Which stage is the feed stage?
1
2
3
partial reboiler (B)

## Slide 6
A McCabe-Thiele solution to a distillation column separating methanol and water is shown. Currently, the feed stage is number _______, but the optimum feed stage is number ________.
4, 3
3, 3
3, 1
3, Boiler
4, 4
Chart: xMethanol
| 0 | 1.2E-2 | 0.02 | 2.5999999999999999E-2 | 3.3000000000000002E-2 | 3.5999999999999997E-2 | 5.2999999999999999E-2 | 7.3999999999999996E-2 | 8.6999999999999994E-2 | 0.108 | 0.129 | 0.16400000000000001 | 0.191 | 0.26800000000000002 | 0.29399999999999998 | 0.35199999999999998 | 0.40200000000000002 | 0.45400000000000001 | 0.502 | 0.56299999999999994 | 0.624 | 0.71699999999999997 | 0.79 | 0.84299999999999997 | 0.85699999999999998 | 0.93799999999999994 | 1
 | 0 | 0.068 | 0.121 | 0.159 | 0.188 | 0.215 | 0.275 | 0.356 | 0.395 | 0.44 | 0.488 | 0.537 | 0.572 | 0.648 | 0.666 | 0.704 | 0.734 | 0.76 | 0.785 | 0.812 | 0.835 | 0.877 | 0.91 | 0.93 | 0.939 | 0.971 | 1

## Slide 7
In column distillation, the limiting operating conditions of minimum reflux and total reflux represent a(n) _________ and a(n) __________ number of stages for a given separation, respectively.
minimum, maximum
infinite, minimum
infinite, maximum
maximum, minimum

## Slide 8
Murphree vapor/liquid efficiencies can exceed one and be less than zero.
true
false

## Slide 9
For a binary distillation column operating at atmospheric pressure, the temperature __________ from the bottom to the top of the column.
increases
decreases
is constant
depends on the separation

## Slide 10
For a binary distillation column operating at constant temperature, the pressure __________ from the bottom to the top of the column.
increases
decreases
is constant
depends on the separation

## Slide 11
An operator is creating a dial to control the reflux ratio in a distillation column. What must be the two values for the limits of the dial?
-1 and 1
0 and 1
1 and
0 and
V
D
L
Dial
Notes: ANSWER: D. Can have total reflux (∞) or single separation (no reflux 𝐿/𝐷=0 ) and anything in between.

## Slide 12
Which of the following plots cannot be used to represent a rectifying section operating line for a distillation column separating a binary mixture? Plots are for more volatile species.
3, 4, 6
4 & 5
4, 5, 6
1 & 2
3, 4, 5, 6
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
1
6
4
5
3
2
Notes: ANSWER: A. The material balance results in 𝑦=𝐿/𝑉 𝑥+𝐷/𝑉 𝑥_𝐷 , which has a slope less than 1 since it’s the rectifying section and some fraction of the vapor is condensed and returned to the column as liquid. The intercept must be greater than or equal to 0 since the distillate flow rate (D) is a fraction of the vapor flow rate (V) (=1 if reflux =0) and the composition (xD). This means plots C and D are not possible due to their slopes >1. F is out because you cannot have a negative slope. The rest are feasible.
slope is 𝐿/𝑉<1
Intercept is 𝐷/𝑉 𝑥_𝐷≥0

## Slide 13
Which of the following plots cannot be used to represent a stripping section for a distillation column separating a binary mixture?
2
1, 2, 3
2, 3, 5
2, 5
All but 4
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
1
6
4
5
3
2
Notes: ANSWER: A. The material balance results in𝑦=𝐿 ̅/𝑉 ̅ 𝑥−𝐵/(𝑉 ) ̅ 𝑥_𝐵, which has a slope greater than 1 since it’s the stripping section and some fraction of the liquid is boiled up and returned to the column as vapor. The intercept must be less than or equal to 0 since both flow rates and composition are positive values. The only plot that doesn’t follow these rules is plot B.
Slope is 𝐿 ̅/𝑉 ̅ ≥1
Intercept is −𝐵/(𝑉 ) ̅ 𝑥_𝐵≤0

## Slide 14
Which of the following tray holes prevents weeping at low vapor flow (or start up of vapor flow)?
tray 1
tray 2
both trays
neither trays
1
2

## Slide 15
A distillation column has 8 stages, a total condenser and a partial reboiler. What is the liquid mole fraction of the more volatile component entering stage 8?
0.04
0.10
0.24
0.80
Chart: Liquid mole fraction (X)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0 | 0.42 | 0.58 | 0.66 | 0.73 | 0.78 | 0.83 | 0.88 | 0.92 | 0.96 | 1
 | 0.92 | 0.52
 | 0.04 | 0.73
0 1 | 0 | 1
 | 0.92 | 0.86783
 | 0.86783 | 0.86783
 | 0.92 | 0.92
 | 0.86783 | 0.81565
 | 0.81565 | 0.81565
 | 0.81565 | 0.76783
 | 0.76783 | 0.76783
 | 0.76783 | 0.7287
XY diagram for more
volatile component

## Slide 16
Chart: Liquid mole fraction (X)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0 | 0.42 | 0.58 | 0.66 | 0.73 | 0.78 | 0.83 | 0.88 | 0.92 | 0.96 | 1
 | 0.92 | 0.52
 | 0.04 | 0.73
0 1 | 0 | 1
 | 0.92 | 0.86783
 | 0.86783 | 0.86783
 | 0.92 | 0.92
 | 0.86783 | 0.81565
 | 0.81565 | 0.81565
 | 0.81565 | 0.76783
 | 0.76783 | 0.76783
 | 0.76783 | 0.7287
A distillation column has 8 stages, a partial condenser and a total reboiler. What is the liquid mole fraction of the more volatile component entering stage 8?
0.04
0.10
0.24
0.80
XY diagram for more
volatile component

## Slide 17
What is the efficiency of a column that we has a partial condenser, a partial reboiler, and 6 physical trays in the column?
67%
50%
33%
16%
Chart: Liquid mole fraction (X)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0 | 0.42 | 0.58 | 0.66 | 0.73 | 0.78 | 0.83 | 0.88 | 0.92 | 0.96 | 1
 | 0 | 1
 | 0.9 | 0.74
 | 0.14 | 0.74
 | 0.9 | 0.9
 | 0.9 | 0.82533
 | 0.82533 | 0.82533
 | 0.82533 | 0.74
 | 0.74 | 0.74
 | 0.74 | 0.50522
 | 0.50522 | 0.50522
 | 0.50522 | 0.14
XY diagram for more
volatile component

## Slide 18
Chart: Liquid mole fraction (X)
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0 | 0.42 | 0.58 | 0.66 | 0.73 | 0.78 | 0.83 | 0.88 | 0.92 | 0.96 | 1
 | 0 | 1
 | 0.9 | 0.74
 | 0.14 | 0.74
 | 0.9 | 0.9
 | 0.9 | 0.82533
 | 0.82533 | 0.82533
 | 0.82533 | 0.74
 | 0.74 | 0.74
 | 0.74 | 0.50522
 | 0.50522 | 0.50522
 | 0.50522 | 0.14
What is the optimal feed location (tray #) for a column with a partial condenser, a partial reboiler and 33% tray efficiency if the feed is saturated liquid at zF = 0.62?
1
2
3
4
5
XY diagram for more
volatile component

## Slide 19
Which feed condition minimizes the difference between partial reboiler and total condenser duties for an ideal binary separation in a distillation column?
supercooled liquid
saturated liquid
saturated vapor
superheated vapor

## Slide 20
Which of the following material balance relationships are true for a binary distillation column operating with a saturated liquid feed, a total condenser and partial reboiler?
(R = reflux ratio = L/D)
= D - F
= R*D
= R*D + F
= R*D + F - B
F
D
B
V
L
V
L

## Slide 21
A distillation column operates with a saturated liquid feed, F1, and a reflux ratio of 2. If another saturated liquid stream is fed at a lower stage (F2), how does the slope of the rectifying operating line change?
decreases
increases
remains the same
depends on quality of F2
F1
R = 2
F2

## Slide 22
A distillation column with a total condenser and partial reboiler separates a binary mixture. Lowering the reflux ratio decreases the tray efficiency. The number of trays needed to achieve the same separation as before ________.
increases
decreases
remains the same
depends on reflux ratio

## Slide 23
When performing separation under vacuum in a column distillation, a _______ column should be used since the pressure drop across this column is lower.
packed
trayed
negligible difference
packed
trayed

## Slide 24
Which is most likely true for a liquid passing along a tray in a column distillation for short residence times and uneven mixing? x is the mole fraction of the more volatile component.
xout > x1
xout < x1
xout = x1

## Slide 25
Which of the following results in only vapor products (D and B)?
1) Partial condenser 2) Total condenser
3) Partial reboiler 4) Total reboiler
5) Total reflux 6) Total boilup
1 & 3
5 & 6
2 & 4
2 & 6
4 & 5
F
D
B
V
L
V
L
Note: not drawn for all setups

## Slide 26
The McCabe-Thiele solution is shown for a distillation column with a saturated liquid sidestream (S) product. Keeping reflux constant, what happens to the number of stages needed in the rectifying section if the flow rate of S increases?
increases
decreases
no change
Chart: x MeOH
| 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
 | 0 | 0.42 | 0.58 | 0.66 | 0.73 | 0.78 | 0.83 | 0.87 | 0.92 | 0.96 | 1
 | 0 | 1
 | 0.75 | 0.81
 | 0.5 | 0.63
 | 0.95 | 0.81
 | 0.81 | 0.63
 | 0.63 | 0.05
 | 0.97 | 0.97
 | 0.97 | 0.9395
 | 0.9395 | 0.9395
 | 0.9395 | 0.894
 | 0.894 | 0.894

## Slide 27
Which of the following ideal binary distillation columns uses the most energy? Feed conditions, pressure, reflux ratio, and top and bottoms compositions are constant.
D. No difference
A
B
C

## Slide 28
For the following distillation system, which of the following component pairs are designated as the light key (LK) and heavy key (HK)?
(Note: Components are in order of volatility, = signifies a double bond)
C1 and C2=
C1 and nC4
C2 and C3=
C2= and C2
Distillation
C1
C2=
C2
C3=
C3
nC4
500
1,250
1,000
100
50
25
kmol/h
C3= 2.5 kmol/h
C2 0.5 kmol/h
Notes: ANSWER: C. C_2 is designated with a minimal amount in the bottoms stream, so it must be light key and 𝐶_3= is then the heavy key since it specified in the top stream.

## Slide 29
Compound R and compound S are separated in a batch distillation process. Given that PRsat < Pssat and the solution is ideal, the first drop of distillate will be enriched in ____________.
compound R
compound S
depends on the initial mole fractions
xR, xS
Q

## Slide 30
Compound R and compound S are separated by batch distillation. Given PRsat < Pssat and the solution is ideal, the mole fraction of S in the distillate _________ as the process proceeds.
increases
decreases
depends on initial mole fractions
xR, xS
Q

## Slide 31
Compound R and compound S are separated through batch distillation. Given PRsat < Pssat and the solution is ideal, the mole fraction of S in the feed-stock _________ as time proceeds.
increases
decreases
depends on initial mole fractions
xR, xS
Q

## Slide 32
A 100-mol mixture of benzene and toluene are fed into a batch distillation still, which is heated to keep the boil-up rate constant. Which of the following does not change during the distillation?
distillate composition
bottoms composition
still temperature
distillate flow rate
none of the above

## Slide 33
The amount of vapor product produced in a flash distillation process is dependent on _________.
the feed composition
the temperature of the flash operation
the temperature of the feed
A & B
All of the above

## Slide 34
0.08
0.40
0.55
0.62
Given a feed of 40 mol% EtOH, what is the maximum ethanol vapor fraction achievable in a flash drum?

## Slide 35
For a flash distillation at its bubble point, what fraction (V/F) of a feed stream becomes vapor?
V/F ≈ 0, all liquid
V/F ≈ 1, all vapor
Cannot determine

## Slide 36
If three flash tanks were stacked, how would the pressures of each tank be set to maximize separation efficiency?
P1 > P2 > P3
P1 > P3 > P2
P1 < P2 < P3
P1 < P3 < P2
P1
P2
P3
V1
L1
V2
V3
L2
L3
liquid feed
liquid
liquid

## Slide 37
A liquid feed containing 20 mol% MeOH enters a flash tank at 3 psia. If we compress the exiting vapor to 6 psia then send it to another tank operating at 4 psia, what is the vapor mole fraction of MeOH
leaving the
2nd tank?
0.1
0.2
0.4
0.6
0.99

## Slide 38
What will happen if we recycle the liquid stream from tank 2 (L2) back to tank 2? (y is the mole fraction of the more volatile component in the vapor)
y2 decreases
y2 increases
Ratio of L/V produced from tank 2 increases
Ratio of L/V produced from tank 2 decreases
A & C
P1
P2
P3
V1
L1
V2
V3
L2
L3
liquid feed
liquid
liquid
Notes: ANSWER: C. By recycling L2 we lower the total feed composition 𝑧_𝐹 of MeOH (since L2 is enriched in lower volatility component).

## Slide 39
How should the temperature for each stage be set for stacked flash tanks under isobaric conditions?
T1 > T2 > T3 > T4 > T5
T1 < T2 < T3 < T4 < T5
T1 < T2 < T3 > T4 < T5

## Slide 40
Which vapor flow rate is larger, V1 or V2?
V1
V2
V1 = V2