Homework, BIEN 501

Figure 1 is a representation of a carotid artery flow waveform that is in terms of the centerline velocity.  The waveform repeats with a frequency of 1 Hz (pulse rate 60 beats/min).  The waveform can be represented by a Fourier decomposition as follows:

where

40 cm/sec

20 cm/sec,

18 cm/sec,

4 cm/sec,

- Based on this waveform and the assumption that mean wall shear stress is 15 dynes/cm2, estimate the radius of the artery.  Assume that the dynamic viscosity of blood is 0.035 g/(cm-sec) and that the density of blood is 1.05 g/cm3.  (Note: you can use the Poiseuille flow solution with velocity = 40 cm/sec; there is no need to use the complete Fourier decomposition for this first part – why?).

- Use the Fourier representation to calculate the solution for Womersley flow based on this waveform.  Calculate and plot the velocity profile as a function of radial position for the following three times within the waveform:

- Early acceleration (t=0)

- Peak systole (t = 0.2 sec)

- Mid deceleration (t=0.3 sec)

- End deceleration (t=0.4 sec)

You can perform all of these calculations in Matlab, which has the Bessel function that you will need.  For example, besselj(0,r) computes the Bessel function .

# Text boxes

Figure 1: Approximation of a carotid artery flow waveform.