Circle the most correct answer to each question.  An answer is considered to be “correct” if it is within 1% of the correct answer.

- According to a Poiseuille flow estimate, what is the flow rate in an artery that has a radius of 0.3 cm, a dynamic viscosity of 0.035 cm2/s and a wall shear stress of 15 dynes/cm2?

  - 5.33 ml/s

  - 9.09 ml/s

  - 7.20 ml/s

  - 2.01 ml/s

e. none of the above

- Using the Poiseuille approximation for wall shear stress, what pressure drop will cause a cross-sectional averaged velocity of 32.1 cm/s in an artery with a radius of 0.3 cm and a length of 20 cm, assuming that the blood has a constant dynamic viscosity of 0.035 cm2/s?

  - 200 mm Hg

  - 2000 mm Hg

  - 2000 dynes/cm2

  - 1340 dynes/cm2

none of the above

- A sphere of radius  rotates in the  direction (about the  axis) in an otherwise stagnant fluid.  A correct boundary condition for this problem is:

a.  at .

b.  at .

c.  at

d.  as

e. none of the above

- An additional boundary condition for the rotating sphere problem is:

a.  at .

b.  at .

c.  at .

d.  at .

e. none of the above

- The choice of coordinate systems in a fluid mechanical problem is dictated by:

  - The continuity equation.

  - The momentum equation.

  - The energy equation.

  - The boundary conditions.

e. none of the above

- The stream function is derived from:

  - The momentum balance.

  - The continuity equation.

  - Poiseuille’s law.

  - Newton’s law of viscosity.

none of the above.

- Use of the stream function in a fluid mechanical problem:

  - Increases the number of variables while increasing the order of the equation.

  - Decreases the number of variables while increasing the order of the equation.

  - Increases the number of variables while decreasing the order of the equation.

  - Decreases the number of variables while decreasing the order of the equation.

  - Has no effect on the number of variables or the order of the equation.

- The stream function is useful when:

  - The flow is three-dimensional.

  - The flow is two-dimensional (i.e. planar or axisymmetric).

  - All components of velocity are zero at one of the boundaries.

  - Pressure is negligible.

  - none of the above.

Assuming that there are no changes in the -direction, the expression for  in cylindrical coordinates reduces to:

  - 0

  - none of the above

- On taking the limit of the following expression as ,

one obtains:

a.

b.

c.

d.

e. none of the above

- A primary reason for the non-Newtonian properties of blood is:

  - The formation of rouleax by the red blood cells.

  - The presence of albumen.

  - Repulsive forces between red blood cells.

  - Dark energy.

  - none of the above

- The equation of continuity states that:

  - Force is continuous throughout the volume of interest.

  - Density is constant throughout a control volume.

  - Velocity is zero on any non-moving boundary.

  - The net amount of matter entering a control volume through the surface is equal to the gain in matter within that volume.

  - None of the above.

- Consider a flat disk of infinite radius rotating at constant angular velocity above a stationary surface, as shown to the right.  The equation for momentum for the Newtonian fluid between the plates in the  direction is:

  - non-linear

  - dependent on

  - all of the above

  - none of the above

- Assuming that the momentum balance in the  direction for a rotating flow is:

,

let .  Then the equation for the  dependence of  is:

- non-linear

- , where  is an arbitrary function of .

- None of the above.

- A monocyte of radius 10 (m and density  g/cm3 is suspended in saline ( g/cm3,  g/(cm-s)) and centrifuged at 50 x g (50 times the acceleration of gravity).  Assuming that the Stokes flow relationship for flow over a sphere is appropriate for this situation, how long does it take for the monocyte to travel 4.9 cm (to the bottom of the centrifuge tube)?

  - 0.09 seconds

  - 4.28 seconds

  - 90 seconds

  - 21 minutes

none of the above

- You have an instrument that can directly measure velocity, but cannot directly measure acceleration.  If you need to know the acceleration of a fluid in the  direction at a given point you should:

  - Measure velocity as a function of time and take the derivative of the output of your instrument.

  - Measure velocity at two nearby points,  and  and approximate

acceleration as .

  - Add the result of a. above to the result of b. above.

  - Multiply the result of a. above by the result of b. above.

  - None of the above.

- The flux of momentum per unit volume through a surface is:

  - Equal to the flux of momentum per unit volume out of the surface.

  - Normal to the surface.

  - Equal to the momentum per unit volume times the velocity normal to the surface integrated over the surface.

  - The cause of the nonlinear terms in the momentum equation.

  - Both c and d.

- The momentum equation used in the book and typically used in fluid mechanical applications:

  - is written in terms of a Lagrangian frame of reference.

  - is written in terms of an Eulerian frame of reference.

  - is linear in all practical applications.

  - contains 3 unknown variables.

  - none of the above.

- The expression

  - is the continuity equation for incompressible flow.

  - is a single equation.

  - involves 3 unknown variables.

  - contains  as one term.

  - all of the above.

- The expression

  - contains 3 separate vector components

  - contains 9 separate vector components

  - reduces to one scalar component

  - becomes zero for incompressible flows

  - none of the above

# Text boxes

axis

direction