Modeling

- Give an example of a physiological model that is relevant to your device:

- Draw a sketch that describes the geometry of the model.

- What general engineering field or fields does the model relate to (e.g. transport, solid mechanics, fluid mechanics, electrical engineering, probability).

- What are the known parameters that will go into your model (inputs)?

- What quantitative data will be sought through the use of the model?

- Give an example of a non-physiological model that is relevant to your device, and do a. through d. above for this model.

- To measure cardiac output, a physician inserts a catheter into the left atrium, injects saline at room temperature, and measures the temperature in the aorta.  Assume that the situation can be modeled as below:

- Derive an expression for the temperature Tout as a function of time, assuming that the saline inflow is constant for a given period of time (tin)  and zero otherwise.

- Determine the relationship between the area under the curve (T vs. time) and the flow rate.

- State any assumptions that were necessary in your analysis.

Steven A. Jones

Biomedical Senior Design

Louisiana Tech University

Last Updated February 22, 2005

<< Back to Senior Design Course Outline Page

# Text boxes

Blood Flow In, T=Tin=constant

Saline  In, T=Ts(t)

Blood Flow Out, T=Tout(t)

Complete Mixing within Heart