March 29, 2005

Product Liability

- Homework:  (do in groups)

Problems 1-9, pages 73-75 in Middendorf and Engleman.

Note: You should keep problem 1 to include in your final report.

- Vocabulary:

- Privity

- Plaintiff

- Defendant

- Landmark Case

- Tort

- Warranty

- Implied warranty

- Disclaimer

- Express Warranty

- Strict Liability

- Forseeable use or Misuse

- Trier of fact

- Deposition

Ultimate Issue

3. Landmark Cases

| Case | Concept Revised | Decision |
| --- | --- | --- |
| MacPherson v. Buick Motor Co. (1916) (Broken Axel) | Manufacturer is not responsible since he did not sell directly to the plaintiff. | Privity is not necessary if the manufacturer knows that the item will be used by someone other than the purchaser |
| Henningsen v. Bloomfield Motors, Inc. (1960). (Steering Defect) | Plaintiff must demonstrate negligence on the part of the manufacturer. | There is an implied warranty when a thing is marketed. |
| Greenman v. Yuba Power Products (1962) Defective lathe set screws. | No strict liability, but implied warranty | A manufacturer is strictly liable when an article he placed on the market proves to have a defect. (deep pockets) |
| May v. Columbian Rope Co. | Need to specify the defect. | res ipsa loquitur (“The thing speaks for itself”). |

- Questions to consider:

- What can happen while the product is still in its package (aluminum doors).

- What physical changes might happen during normal use of the product? (Hammer).

- What (mis)uses might be found by someone who is not the principle user. (Lawn tractor, vaporizer-fire, vaporizer-scalding, battery explosion)

- What problems might arise prior to shipment? (industrial mixer).

- Interlock mechanisms.

- Button configurations

- Will the ultimate user vary in dimensions and what will be the result?

- Football helmet

- Air bags

4. Guidelines to reduce product liability risk

- Include safety as a design criterion.

- Design to nationally recognized standards.

- Use materials of sufficient quality and tolerances.

- Perform analysis to determine whether electrical, mechanical, and thermal stresses are within published limits.

- Test the device using accelerated aging tests.

- Conduct a design review with experts in distribution, installation, use, manufacturing, human dangers after discard, environmental dangers after discard.

- Make a failure and hazards analysis of the product for each stage of product life.

- Make a worst-case analysis , assuming that all tolerances will be off in the worst possible way.

- Submit the product to an independent testing laboratory.

- Keep production engineers informed of all specifications.  Annotate any specific requirements. (hardness, elimination of burrs, etc.)

- Make a complete permanent record of the product history.

- Document any conflicts between risk and utility.  Document design changes that could be made, but that would make the product noncompetative (economically or functionally).

- Use warning labels on the product when appropriate.

- Supply unambiguous instructions for proper installation.  Test instructions on the least common denominator.

- Determine any maintenance requirements.

- Have all products inspected after manufacture.  Use functional testing.

- Notify quality control supervisor of manufacturing errors.  Keep manufacturing equipment in good order (tools, dies, etc.).

- Test to make sure the product is adequate even when mass produced.

- Guard against overstatements of product performance.

- Encourage sales/service personnel and dealers to report all complaints.

- Is a defect alleged?

- If so, what is the defect?

- How did the defect lead to the complaint?

- What was the nature and extend of the injury or economic loss?