## Slide 1
Which is desirable in designing an absorption process?
high pressure, high temperature
high pressure, low temperature
low pressure, high temperature
low pressure, low temperature
liquid out
gas out
gas in
liquid in
Notes: ANSWER: C. An effective absorption process removes a species from the vapor phase into the liquid phase. Low temperatures and high pressures favors this thermodynamic equilibrium. 𝐾=(𝛾𝑃^𝑠𝑎𝑡)/𝑃, 𝐴=𝐿/𝐾𝑉
P increases, K decreases, A increases
T decreases, 𝑃^𝑠𝑎𝑡 decreases, K decreases, A increases
1

## Slide 2
Which of the following is an appropriate plot for a physical absorption process for a dilute species? The black line is the operating line and the blue line is the equilibrium line.
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
A
B
C
D
Notes: 2

## Slide 3
For this physical absorption process, which point(s) lie(s) on the operating line for the McCabe-Thiele graphical solution? (Note: x and y represent liquid and gas mole fractions, respectively)
(xN, y1)
(x0, y1)
(x0, yN+1)
(xN, yN+1)
B and D
S, x0
S, xN
G, y1
G, yN+1
Notes: 3

## Slide 4
A dilute species is being absorbed. Equilibrium is modeled using Henry’s law. Which has the greatest absorption factor (A = L/KV)?
operating line = black; equilibrium line = blue
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
Liquid mol fraction
Vapor mol fraction
0
A
B
C
D
Notes: 4

## Slide 5
A process calls for 98% recovery of solute B from a vapor stream using absorption. The current design (100 L) can accomplish this, but an engineer wants to use less absorbent. What is the minimum amount of liquid absorbent (L) that can be used assuming the number of stages are
not limiting?
50
33
25
10
< 10
Vapor mol fraction
Liquid mol fraction
L = 100
L = 50
L = 33
L = 25
L = 10
Equilibrium line
Notes: 5

## Slide 6
Several assumptions are made during McCabe-Thiele analysis of an absorber including constant molar overflow and an isothermal system. What additional assumption is made for an analytical solution for dilute systems?
Murphree efficiencies for every stage are 1.
The solvent stream is fed as a pure liquid/vapor.
The equilibrium line is linear.
No additional assumptions are made.
Notes: 6

## Slide 7
For a fixed purity/yield, counter-current absorption processes require __________ solvent than cross-flow processes.
less
more
dependent on the scenario
Notes: 7

## Slide 8
For a fixed solvent quantity, counter-current absorption processes can achieve ________ purity and yield than cross-flow processes.
higher
lower
dependent on the scenario
Notes: 8

## Slide 9
For absorption and stripping processes, appropriate solutions can always be obtained by treating the system as concentrated as opposed to dilute
(< 1 wt%).
true
false
Notes: 9

## Slide 10
What is heat exchanger B doing?
heating
cooling
nothing (not needed)
depends
stripping gas
gas to be treated
A
B
spent
solvent
treated gas
Notes: 10

## Slide 11
What is heat exchanger A doing?
heating
cooling
nothing (not needed)
depends
stripping gas
gas to be treated
A
B
spent
solvent
treated gas
Notes: 11

## Slide 12
The absorption factor, AN, for a given stage and component for this column is shown below:
where K is the thermodynamic
K-value and N represents the stage #. What is the relationship
between A and the stripping factor, S?
AN = SN
AN = 1/SN
AN = S1
AN = 1/S1
liquid
L1
vapor
VN+1
vapor
V1
liquid
LN
1
2
3
N-2
N-1
N
Notes: 12

## Slide 13
The recovery factor, FA, for an absorption column is shown below:
where is the molar flow rate of the
absorbed species. A perfect
separation means FA is _____.
0
0.5
1
Infinity
liquid
L1
vapor
VN+1
vapor
V1
liquid
LN
1
2
3
N-2
N-1
N
Notes: 13

## Slide 14
For this absorption column, which of the following must be true?
VLE reached at each stage
only one solute absorbed
absorbent not vaporized
absorbate prefers liquid phase
all of the above
X0, L’
YN+1, V’
Y1, V’
XN, L’
1
N
n
Notes: 14